## Slide 1: SIVAP Intelligent System based on Machine Learning and Computer Vision for the Optimization of the Manufacturing Process of Porcelain
Romanian Research Ministry
BRIDGE GRANT – KNOWLEDGE TRANSFER TO AN ECONOMIC AGENT
UEFISCDI PN-III-P2-2.1-BG-2016-0333
Period of implementation: October 2016- October 2018

## Slide 2: Program Challenges BRIDGE GRANT – KNOWLEDGE TRANSFER TO AN ECONOMIC AGENT
Program goal:
  To increase the competiveness of economic agents by knowledge transfer from research institutes and universities
Objectives
  To connect the expertise of universities with the economic agent necessities;
  To accomplish student internships at the economic agent;
  To develop entrepreneurial skills of researchers;

## Slide 3: Project overview SIVAP Intelligent System based on Machine Learning and Computer Vision for the Optimization of the Manufacturing Process of Porcelain
What
  Knowledge transfer project to IPEC to optimize the manufacturing process of porcelain.
How
  An intelligent system based on machine learning and computer vision will optimize and innovate the current production flow.
Objectives
  reducing the manufacturing time at each processing phase
  optimizing the production efficiency by eliminating defective products
  improving the monitoring and control system of the entire flow by adding new functionalities to the current computer vision system
  increasing the innovation capacity of the economic agent.
Results
  monitoring and quality control system implemented in real time and its integration into the company’s decision-making system
  defects will be identified and classified at every operational phase.

## Slide 4: SIVAP Concept & Approach:
The optimized system will be based on the robot-computer vision architecture and will include:
  real-time high-speed processing of product images
  a global autonomous behaviour, context and task dependent self-learning that will be adaptive to the work environment

## Slide 5: SIVAP – Expertise
Artificial intelligence:
  Robotics
  Machine learning
  Computer vision
  Stochastic modelling
System engineering
  Multi-agent systems
  Expert systems
  Electronic systems

## Slide 6: SIVAP Integrated in the Production Flow
SIVAP will be integrated in the production flow of porcelain as follows:
Step 1. Product reaches the inspection system;
Step 2. Product is illuminated + Sensor detects the product and sends a signal to the computing vision system;
Step 3. Computing Vision system receives the image from sensors;
Step 4. Various algorithms running on the artificial vision system process and analyze received images;
Step 5. Vision system sends signals to an industrial robot to remove the product if it is defective;
Step 6. Human operator analyses the acurracy of the rejected products and do statistics

## Slide 7: Vision Inspections for Defects - Proposed approaches
Enhancement of the capabilities of the existing FANUC vision system 2D cameras + software modules)
Adaption of the existing 3D cameras for defect detection
Configuration of a new automate inspection technique by using Nation Instruments equipment
Study of Deep learning techniques for defect identification
Study of thermo-imaging after phases: Burning 1 and 2.

## Slide 12: Defect detection with various algorithms implemented in Vision systems

## Slide 13: Defect detection with various algorithms implemented in Vision systems

## Slide 14: Defect detection with various algorithms implemented in Vision systems

## Slide 15: Defect detection with various algorithms implemented in Vision systems

## Slide 16: Defect detection with various algorithms implemented in Vision systems

## Slide 17: Automated comparison with standard product

## Slide 18: Automated comparison with a standard product

## Slide 19: Automated comparison with a standard product

## Slide 20: NI Vision hardware and software

## Slide 22
Performance

## Slide 24
Research Software
Extra benefits:
(for the first year with the possibility of extension)
- Fast technical support
- Free access to online trainings
- Access to online software
- Free upgrades to new SW

## Slide 25: Machine Learning

## Slide 26: Deep Learning

## Slide 27: Deep neural networks

## Slide 28: Training data- Binary classification problem

## Slide 29: Training data- Binary classification problem

## Slide 30: Future work
Automated recognition of defect type by machine learning and data mining techniques;
Increase of performance of existing 2D cameras by design and implementation of software for defect detection in the control system;
Increase of performance of existing 3D cameras by design and implementation of software for defect detection after burning of products;
New vision system architecture designed for the pressing phase and for final sorting of products;

## Slide 31: Thermographic testing
A thermovision camera is used for observing and recording over time
the temperature distribution on the surface of the object inspected.
Temperature differences can indicate hidden defects in the material structure, such defects being due to faulty production.
The camera indications are not assessed directly, but compared to
thermograms of flawless objects in similar operating conditions.
The user obtains information on the temperature of each pixel on the
basis of physical data entered, such as the emissivity of the object, and most importantly, the intensity of electromagnetic radiation reaching the camera detector.

## Slide 32: Thermographic testing
Active thermography has become a highly functional measurement
method thanks to modern materials used in the construction of
thermovision cameras, computerised recording, processing and data
saving techniques, and artificial intelligence.

## Slide 33: Project team -UAB
Adriana Birlutiu, UAB – machine learning
Adrian Burlacu, Univ.Tehnică Gheorghe Asachi din Iaşi - computer vision
Santiago Garrido, Universitatea Carlos III Madrid – robotics
Manuella Kadar, UAB – multi-agent systems
Ricardo Jardim-Goncalves, New University of Lisbon – system interoperability
Adrian Tulbure, UAB – energy consumption
Gheorghe Marc, UAB – electronics
Angel Garrido, Universitatea UNED, Madrid – fuzzy systems
Lucian Popa, UAB – mathematical modelling
Mihai Oltean, UBB Cluj - robotics

## Slide 34: Project team -IPEC
Cristian Covaciu – General Manager, Project Coordinator
Andrei Corb - computer vision & robotics
Adriana Giurcă – quality control
Andreea Botinanț - assistant